Dataset size: 900 projections, 511 sinograms
Single disk test performed on data residing on one disk in node (not OS disk)
NFS test performed on data residing on a RAID 5 set served over NFS
Performed on 1 x 8 CPU core node only
No GPU used in calculation
Avg time is the time per process to complete its assigned subset (projection or sinogram) – error bars indicate deviation across processes.
Total time is the time taken to complete the section (background removal, sinogram creation, sinogram reconstruction) as a function of the number of processes running.
I/O bound stage
CPU bound stage
Single disk and NFS tests

---
Read raw image
file
Determine
background file
Remove
background
Write image
file
Background removal
n parallel processes
time (secs)
~12 min
~3 min
Background removal – single disk vs NFS

---
Read all raw
image files
Write sinogram
 image file
Sinogram creation
n parallel processes
~25 min
~16 min
~5 min
~4min
Sinogram creation – single disk vs NFS

---
Read sinogram
image file
Reconstruct
sinogram
Write
reconstructed
image
Sinogram reconstruction
n parallel processes
~21 min
~3 min
Sinogram reconstruction – single disk vs NFS

---
Background removal
n processes
File size: 4x,
Time: ~6x
~1.6x speedup over
4 threads
Speedup seen as more processes added – IO hit will be seen quickly as nodes / processes added.
Background removal – processes v. image size

---
Background removal
n processes
~ 4x speedup over
single thread
Same as previous graph but with large file (5k x 4k) data removed for clarity.
Background removal – processes v. image size

---
Sinogram creation
n processes
~1.4x speedup over
4 threads
~ 5x speedup over
single thread
Attempted sinogram creation over large files (5k x 4k) – single RAID 5 couldn't handle the IO load.
Sinogram creation – processes v. image size

---
Sinogram reconstruction
n processes
~2x speedup over
4 threads
~ 8x speedup over
single thread
Total run time decreases as more workers added – there will be an IO limit at some point.
Sinogram reconstruction – processes v. image size

---
New image
collected
Experiment
commenced
De-noise,
Remove background,
Create sinograms
As experiment progresses
Once all data has been collected and all sinograms
have been produced
Experiment
complete
Reconstruct sinograms:
N processes,
(Total sinograms / N processes) sinograms per process
Proposed workflow